## Slide 1
Sensor encoding
Discussion workgroup
Session 1
INRC Workgroup
2021
Yulia Sandamirskaya

## Slide 2: Legal Information
Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex​.
Performance results are based on testing as of dates shown in configurations and may not reflect all publicly available ​updates. See backup for configuration details. No product or component can be absolutely secure.
Your costs and results may vary.
Results have been estimated or simulated.
Intel technologies may require enabled hardware, software or service activation.
Intel does not control or audit third-party data. You should consult other sources to evaluate accuracy.
Intel disclaims all express and implied warranties, including without limitation, the implied warranties of merchantability, fitness for a particular purpose, and non-infringement, as well as any warranty arising from course of performance, course of dealing, or usage in trade.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others. ​

## Slide 3: Agenda
Fundamentals of sensor encoding in neuromorphic hardware
  NCL team (20-30min):
    Mike Davies
    Yulia Sandamirskaya
Input from other participants
  3-5 min per statement
"Open mic" discussion
  10 min

## Slide 4: Setting the scene
Know your input signal:
  Dimensionality
  Temporal and value resolution
  Temporal dynamics
  Dynamic range
Know your neuromorphic hardware
  Temporal resolution
  Energy per spike
  Energy per time step per neuron
  Cost of fan-out
  Values resolution
Know your task
  Recognition (classification, discrimination)
  Detection
  Does space, time, or both matter
  What are the scales involved and resolution required
  Constraints, baselines: Latency? Accuracy? Throughput?
  Offline or online processing
Design the sensory pipeline
Sensor
Preprocessing
SNN on chip

## Slide 5: A First Principles Perspective on Neuromorphic Coding Efficiency
N neurons
M axons
F average fanout per axon
0
0
1
0
0
1
0
0
0
0
0
0
1
1
0
0
1
0
0
0
0
0
1
0
0
0
0
0
0
1
T timesteps per symbol, S total spikes
M axons
total SynOps
total NeuronOps
SynOp
NeuronOp
SynOps and NeuronOps are both fundamental to the energy and runtime characteristics of a workload
NeuronOps cost energy
Where (spike activity rate over T timesteps)
Information content (bits) per T timesteps
M. Davies

## Slide 6: Example application: Maximizing information per Joule (Information Theoretic Perspective)
Sparse communication in time maximizes energy efficiency
Efficiency of communicating the symbol to N neurons (bits per Joule):
= Spike activity over the channel (~ probability of transmitting a spike)
= maximal synop energy versus total neuron energy per timestep
Relative efficiency vs =0.5 as cost of communication increases
C = 0.1
C = 1000
1% activity
C = 100
C = 10
5% activity
15% activity
50% activity
Note: for Loihi, can range between ~0.4 (us/timestep) to
~0.03 (ms/timestep)

## Slide 7: For robotics…
A real-time setting, so Interested in power, not energy per computation:
= aggregate spike rate (spikes/s)
Sensor
Preprocessing
Neuromorphic chip
High energy, bandwidth-constrained interface
Goal: Transform input signal to sparsest representation
Want as high as possible (time resolution is expensive)
Want as low as possible (mainly on interface)

## Slide 8: Encoding of measured values with SNs
1. Single-valued data representation
Value =
Input current
Rate-coding
ISI coding
First spike / phase / time coding
To keep in mind:
  Value discretization, resolution, and range
    log scaling for large dynamic range;
    hierarchical representations;
    rescaling the axis of the data depending on the "data-density"/statistics, based on entropy-max function
      need to invert this function later on
  Neurons I/O response (input current -> rate) is non-linear (sigmoid)
    with IF without refractory period: close to linear until it saturates (refractory, or time-discretization)
  Positive and negative values -> two input neurons / paths, or rescaling if no qualitative difference
Examples:
  PID controller
  Spiking D-RL network
  Path integration / SLAM
What happens in the next layer?
Periodicity in sensing (sampling)

## Slide 9: Sensor data as input to an SNN
1b. Single-valued data representation:
  Fourier space (auditory, vibrations, oscillations, frequency content determines the signal)
  Temporal convolutions / correlations
- bank of analog resonators ("cochlea"), Hopf transform
- spike rate -> "energy" in a frequency channel (bank of neurons)
To keep in mind:
- non-linear effects? (dependence on the amplitude)

## Slide 10: Sensor data as input to an SNN
2. Population coding
Why / When is it useful?
  To increase bandwidth / dynamic range
  Dynamics in the encoded space matters
    “Kalman filtering”, DNFs, attractor dynamics
    Noise filtering; working memory; “collective state”; robust representation
    Estimation / Detection / Categorization are of interest, rather than discrimination
  Facilitates learning of (non-linear) mappings between variables
How to apply population coding:
Define "dimension(s)" (velocity, position, force)
  Determined by the task
  Learning: SOM, supervised or unsupervised learning
Introduce receptive fields (with gain and offset) or tuning curves for each neuron in the population
  Sampling of the input space
  Receptive fields can also be learned
Inject current as input, scaled with the tuning curve
  Note the activation (rate, timing) represents the “certainty” of the sensed value now

## Slide 11: Representing values in an SNN on chip
Sparse space code
Value ranges on the drone
0
1
2
3
4
63
…
idx
…
IMU
Identity of an active neuron represents the value
Each spike carries the value
Population code could account for uncertainty

## Slide 12: Sensor data as input to an SNN
3. When we deal with vision or other high-dimensional input
  Deep NN, CNNs
  Shallow sparse representation
Projection into a space where discrimination is facilitated
Making info propagating down-stream sparse
(encoding based on a “training set” to pre-processing dense input into a sparse and compressed input)
Typically high-dimensional input with rich spatial structure (e.g., vision)
Approaches:
  (DNN/CNN: “dense” features) -> take an NPU, use DNN->SNN conversion
  LCA: sparse features
  Our kNN example: Efficient spatial-temporal encoding