## Slide 1: May 2021 Daniel Gutierrez-Galan PhD. student, University of Seville (SPAIN)
Real-time Loihi interface for Neuromorphic Auditory Sensor and ED-Scorbot (RELIAR)
INRC Workgroup “Spike coding for temporal signals”
Notes: Main goals:
  To interface any external event-based neuromorphic sensor implemented on FPGA.
  To use the Neuromorphic Auditory Sensor (NAS) as input for neuromorphic audio applications in real-time.
  To control a robot using spiking PID controllers by using auditory information.

## Slide 2: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 3: Project RELIAR
Real-time Loihi interface for Neuromorphic Auditory Sensor and ED-Scorbot (RELIAR)
Main goals:
  To use the Neuromorphic Auditory Sensor (NAS) as input to Kapoho Bay for neuromorphic audio applications in real-time.
  To control a robot using spiking PID controllers by using auditory information.

## Slide 4: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 5: Neuromorphic Auditory Sensor
Neuromorphic Auditory Sensor (NAS) architecture:
“A binaural neuromorphic auditory sensor for FPGA: A spike signal processing approach”, Jimenez-Fernandez et al., 2016, IEE TNNLS
OpenNAS: Open Source Neuromorphic Auditory Sensor HDL code generator for FPGA implementations, Gutierrez-Galan et al., 2021, Neurocomputing
https://github.com/RTC-research-group/OpenNAS

## Slide 6: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 7: Synthetic Spike Generator
Reverse Bitwise Synthetic Spikes Generator
  Pulse-Frequency Modulation (PFM)
Jiménez-Fernández, Angel, et al. "Building blocks for spikes signals processing." The 2010 International Joint Conference on Neural Networks (IJCNN). IEEE, 1-8.

## Slide 8: Synthetic Spike Generator
3-bit reverse bitwise synthetic spikes generator example:
  Frame time =
  8 clock cycles from
  the clock divider.
  Output: highlighted
  in gray.
Input | Slices counter – Frame time |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
1 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
2 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
3 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
4 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
5 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
6 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
7 | 0 | 4 | 2 | 6 | 1 | 5 | 3 | 7
time
Gomez-Rodriguez, Francisco, et al. "Two Hardware Implementations of the Exhaustive Synthetic AER Generation Method ." 8th International Work-Conference on Artificial Neural Networks (IWANN) 2008.

## Slide 9: Synthetic Spike Generator
Basic behaviors:
Jiménez-Fernández, Angel, et al. "Building blocks for spikes signals processing." The 2010 International Joint Conference on Neural Networks (IJCNN). IEEE, 1-8.

## Slide 10: Synthetic Spike Generator
Basic behaviors:
Jiménez-Fernández, Angel, et al. "Building blocks for spikes signals processing." The 2010 International Joint Conference on Neural Networks (IJCNN). IEEE, 1-8.

## Slide 11: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 12: Hardware setup

## Slide 13: Hardware
36 pins connector (top) for CAVIAR-based connectors.
1
2

## Slide 14: Hardware
Input AER format:
  10 bits for AER data.
  1 bit for AER req.
  1 bit for AER ack.
Both req and ack are low active.

## Slide 15: Software
In ..\nxsdk-apps-0.9.8\nxsdk-apps-0.9.8\nxsdk_modules\dvs\src\
  DVS sensor python class: dvs.py
  DVS sensor C code snip: snips\dvs_default.c
In ..\nxsdk-apps-0.9.8\nxsdk-apps-0.9.8\nxsdk_modules\dvs\tutorials\
  DVS sensor live connection: dvs_live.py
  DVS sensor visualizer: snips\default_visualizer.c
Custom main script (application specific)

## Slide 16: Hardware
Done:
  VHDL code for sending events from NAS to Kapoho Bay & custom PCB.
To do:
  How could we close the loop between NAS and Kapoho Bay for real-time robotic applications?
  Look for the best spike generator parameters according to Loihi features.

## Slide 17: Software
Done:
  Execution of DVS live examples.
  Using NAS’ output events as input of a SNN & real-time visualization (custom visualizer).
To do:
  To adjust NAS’ output firing rate (too high ~30 Mevents/sec).
  Training methods & weights translation from SpiNNaker.

## Slide 18: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 19: Real neuromorphic application
Real-time detection of bursts in neuronal cultures using a Neuromorphic Auditory Sensor and SNNs:
  Rate coding & STDP.
“Real-time detection of bursts in neuronal cultures using a Neuromorphic Auditory Sensor and Spiking Neural Networks”, Dominguez-Morales et al., 2021, Neurocomputing
Notes: A novel neuromor-phic approach for real-time burst detection is proposed and tested on acquisitions from in vitro cultures.The system consists of a Neuromorphic Auditory Sensor, which converts the input signal obtained from electrophysiological recordings into spikes and decomposes them into different frequency bands.

## Slide 20: Outline
Project RELIAR
Neuromorphic Auditory Sensor (NAS)
Synthetic Spike Generator
NAS-Kapoho Bay interface
Real neuromorphic application
Questions & Acknowledgment

## Slide 21: Questions
Thank you very much!
Acknowledgment:
  Yulia Sandamirskaya, Garrick Orchard, and Lyes Khacef, among others.